## Slide 1: 06/07/23 RTS Update Jacob Pew Jay Kim Dr. Loveless

## Slide 2: Summary
Data collection progress
Parameter extraction progress and results
Data analysis examples collected during test runs
  Explanation of how RTS is defined in the python code
Data analysis examples collected post test runs

## Slide 3: Samples Summary
Bank 0:
  10uA : 3168 Samples
  1uA : 2528 Samples
  100nA : 3072 Samples
  10nA : 3072 Samples
  Total : 11840 Samples
Bank 2:
  10uA : 3072 Samples
  1uA : 4736 Samples
  100nA : 3072 Samples
  10nA : 0 Samples
  Total : 10880 Samples
Bank 1:
  10uA : 4805 Samples
  1uA : 416 Samples
  100nA : 544 Samples
  10nA : 3312 Samples
  Total : 9045 Samples
  3072 = 96 rows * 32 columns = whole bank

## Slide 4: Definitions
µ(VRTS) – average amplitude of the RTS seen
RTS – average time spent at RTS amplitude
τ12(ms) – capture/emission time constant
τ21(ms) – capture/emission time constant
τ12/τ21 - Ratio of time constants
µ(N)[Transitions/sample] - Average number of transitions per sample
# of RTS Levels – The highest number of RTS levels seen
# of RTS – Number of signals that were analyzed with RTS for the bank
% RTS - percentage of how many devices showed RTS per bank

## Slide 5: Parameter Extraction Progress
Bank | Column | Rows | Devices | Samples | Ids | W/L | IDS | µ(VRTS) | RTS | τ12(ms) | τ21(ms) | τ12/τ21 | µ(N)[Transitions/sample] | # of RTS Levels
0 | 0-31 | 96 | 3072 | 448 | 10uA | 0.28/0.1, 0.28/8, 1.5/0.1, 1.5/0.35, 1.5/1.6, 1.5/8, 8/0.1, 8/8 | 10uA | 535 | 7.6 | 36.9 | 691 | 0.149 | 56.3 | 3
0 | 0-31 | 96 | 3072 | 2528 | 1uA | 0.28/0.1, 0.28/8, 1.5/0.1, 1.5/0.35, 1.5/1.6, 1.5/8, 8/0.1, 8/8 | 1uA | 772 | 1.3 | 34.5 | 848 | 0.122 | 52.7 | 4
0 | 0-31 | 96 | 3072 | 3072 | 100nA | 0.28/0.1, 0.28/8, 1.5/0.1, 1.5/0.35, 1.5/1.6, 1.5/8, 8/0.1, 8/8 | 100nA | 3010 | 0.026 | 20.4 | 613 | 0.0864 | 45.4 | 4
0 | 0-31 | 96 | 3072 | 3072 | 10nA | 0.28/0.1, 0.28/8, 1.5/0.1, 1.5/0.35, 1.5/1.6, 1.5/8, 8/0.1, 8/8 | 10nA | 1050 | 2.4 | 19 | 447 | 0.132 | 174 | 4
1 | 32-63 | 96 | 3072 | 3072 | 10uA | 0.28/0.1, 0.28/8, 1.5/0.1, 1.5/0.35, 1.5/1.6, 1.5/8, 8/0.1, 8/8 | 10uA | 667 | 3.8 | 57.9 | 946 | 0.12 | 43.7 | 4
1 | 32-63 | 96 | 3072 | 416 | 1uA | 0.28/0.1, 0.28/8, 1.5/0.1, 1.5/0.35, 1.5/1.6, 1.5/8, 8/0.1, 8/8 | 1uA | 1300 | 5 | 52.9 | 341 | 0.237 | 44.3 | 3
1 | 32-63 | 96 | 3072 | 544 | 100nA | 0.28/0.1, 0.28/8, 1.5/0.1, 1.5/0.35, 1.5/1.6, 1.5/8, 8/0.1, 8/8 | 100nA | 1360 | 0.86 | 117 | 2260 | 0.0705 | 33.6 | 3
1 | 32-63 | 96 | 3072 | 784 | 10nA | 0.28/0.1, 0.28/8, 1.5/0.1, 1.5/0.35, 1.5/1.6, 1.5/8, 8/0.1, 8/8 | 10nA | 1930 | 3 | 34.7 | 178 | 0.223 | 72.3 | 4
2 | 64-95 | 96 | 3072 | 3072 | 10uA | 0.42/0.35, 0.42/8, 1.2/0.35, 1.2/0.5, 1.2/0.8, 1.2/8, 8/0.35, 8/8 | 10uA | 1270 | 34 | 95.1 | 735 | 0.396 | 47.1 | 3
2 | 64-95 | 96 | 3072 | 3072 | 1uA | 0.42/0.35, 0.42/8, 1.2/0.35, 1.2/0.5, 1.2/0.8, 1.2/8, 8/0.35, 8/8 | 1uA | 1430 | 33 | 57.6 | 957 | 0.132 | 43.5 | 4
2 | 64-95 | 96 | 3072 | 0 | 100nA | 0.42/0.35, 0.42/8, 1.2/0.35, 1.2/0.5, 1.2/0.8, 1.2/8, 8/0.35, 8/8 | 100nA |  |  |  |  |  |  | 
2 | 64-95 | 96 | 3072 | 0 | 10nA | 0.42/0.35, 0.42/8, 1.2/0.35, 1.2/0.5, 1.2/0.8, 1.2/8, 8/0.35, 8/8 | 10nA |  |  |  |  |  |  | 
3 | 96-127 | 96 | 3072 | 0 | 10uA | 0.42/0.35, 0.42/8, 1.2/0.35, 1.2/0.5, 1.2/0.8, 1.2/8, 8/0.35, 8/8 | 10uA |  |  |  |  |  |  | 
3 | 96-127 | 96 | 3072 | 0 | 1uA | 0.42/0.35, 0.42/8, 1.2/0.35, 1.2/0.5, 1.2/0.8, 1.2/8, 8/0.35, 8/8 | 1uA |  |  |  |  |  |  | 
3 | 96-127 | 96 | 3072 | 0 | 100nA | 0.42/0.35, 0.42/8, 1.2/0.35, 1.2/0.5, 1.2/0.8, 1.2/8, 8/0.35, 8/8 | 100nA |  |  |  |  |  |  | 
3 | 96-127 | 96 | 3072 | 0 | 10nA | 0.42/0.35, 0.42/8, 1.2/0.35, 1.2/0.5, 1.2/0.8, 1.2/8, 8/0.35, 8/8 | 10nA |  |  |  |  |  |  | 

## Slide 6: Statistical RTS Summary
Bank | Bias Condition | FET Type | # of RTS | Samples | % RTS
0 | 10uA | BLOCK_NMOSLV | 35 | 448 | 7.8%
0 | 1uA | BLOCK_NMOSLV | 159 | 2528 | 6.3%
0 | 100nA | BLOCK_NMOSLV | 47 | 3072 | 1.5%
0 | 10nA | BLOCK_NMOSLV | 166 | 3072 | 5.4%
1 | 10uA | BLOCK_NMOSLV_DNWELL | 240 | 3072 | 7.8%
1 | 1uA | BLOCK_NMOSLV_DNWELL | 17 | 416 | 4.1%
1 | 100nA | BLOCK_NMOSLV_DNWELL | 28 | 544 | 5.1%
1 | 10nA | BLOCK_NMOSLV_DNWELL | 16 | 784 | 2.0%
2 | 10uA | BLOCK_NMOSHV | 213 | 3072 | 6.9%
2 | 1uA | BLOCK_NMOSHV | 635 | 3072 | 20.7%
2 | 100nA | BLOCK_NMOSHV |  |  | 
2 | 10nA | BLOCK_NMOSHV |  |  | 
3 | 10uA | BLOCK_NMOSHV_DNWELL |  |  | 
3 | 1uA | BLOCK_NMOSHV_DNWELL |  |  | 
3 | 100nA | BLOCK_NMOSHV_DNWELL |  |  | 
3 | 10nA | BLOCK_NMOSHV_DNWELL |  |  | 

## Slide 7
Bank 2
Vg = 3.3V Vdd = 3.3V Sample Rate = 2 kHz
Ids = 100 nA
Signal is filtered using the savgol filter from scipy package.
Signal is flagged with RTS because the histogram of the filtered signal has more than 1 peak.
1/f noise is calculated using Welch's method from scipy.signal.welch.
Time constants are calculated by finding the peaks of the signal but needs work because it detects too many peaks.

## Slide 8
Bank 2
Vg = 3.3V Vdd = 3.3V Sample Rate = 2 kHz
Ids = 100 nA
Steady state is assumed to be the portion of the signal that relates to the highest peak of the histogram.

## Slide 9
Bank 2
Vg = 3.3V Vdd = 3.3V Sample Rate = 2 kHz
Ids = 100 nA
A signal flagged for RTS that may not be RTS.

## Slide 10
Bank 2
Vg = 3.3V Vdd = 3.3V Sample Rate = 2 kHz
Ids = 100 nA

## Slide 11: Bank 1 Ibias = 10uA Extracted Data

## Slide 12: Bank 1 Ibias = 10uA Aggregate Data

## Slide 13: Bank 1 Ibias = 1uA Extracted Data

## Slide 14: Bank 1 Ibias = 1uA Aggregate Data

## Slide 15: Bank 1 Ibias = 100nA Extracted Data

## Slide 16: Bank 1 Ibias = 100nA Aggregate Data

## Slide 17: Bank 1 Ibias = 10nA Extracted Data

## Slide 18: Bank 1 Ibias = 10nA Aggregate Data

## Slide 19
Appendix

## Slide 20: Bank 0 RTS Data Collection Progress
Bank | Type | W/L | Column | Bias Condition | Samples | Bias Condition | Samples | Bias Condition | Samples | Bias Condition | Samples
0 | nshort | 0.28/0.1 | 0,1 | 10 uA | 288 | 1uA | 248 | 100 nA | 192 | 10 nA | 192
0 | nshort | 0.28/8 | 2,3 | 10 uA | 192 | 1uA | 152 | 100 nA | 192 | 10 nA | 192
0 | nshort | 1.5/0.1 | 4,5 | 10 uA | 192 | 1uA | 152 | 100 nA | 192 | 10 nA | 192
0 | nshort | 1.5/0.35 | 6,7 | 10 uA | 192 | 1uA | 152 | 100 nA | 192 | 10 nA | 192
0 | nshort | 1.5/1.6 | 8,9 | 10 uA | 192 | 1uA | 152 | 100 nA | 192 | 10 nA | 192
0 | nshort | 1.5/8 | 10,11 | 10 uA | 192 | 1uA | 152 | 100 nA | 192 | 10 nA | 192
0 | nshort | 8/0.1 | 12,13 | 10 uA | 192 | 1uA | 152 | 100 nA | 192 | 10 nA | 192
0 | nshort | 8/8 | 14,15 | 10 uA | 192 | 1uA | 152 | 100 nA | 192 | 10 nA | 192
0 | nshort_l | 0.28/0.1 | 16,17 | 10 uA | 192 | 1uA | 152 | 100 nA | 192 | 10 nA | 192
0 | nshort_l | 0.28/8 | 18,19 | 10 uA | 192 | 1uA | 152 | 100 nA | 192 | 10 nA | 192
0 | nshort_l | 1.5/0.1 | 20,21 | 10 uA | 192 | 1uA | 152 | 100 nA | 192 | 10 nA | 192
0 | nshort_l | 1.5/0.35 | 22,23 | 10 uA | 192 | 1uA | 152 | 100 nA | 192 | 10 nA | 192
0 | nshort_l | 1.5/1.6 | 24,25 | 10 uA | 192 | 1uA | 152 | 100 nA | 192 | 10 nA | 192
0 | nshort_l | 1.5/8 | 26,27 | 10 uA | 192 | 1uA | 152 | 100 nA | 192 | 10 nA | 192
0 | nshort_l | 8/0.1 | 28,29 | 10 uA | 192 | 1uA | 152 | 100 nA | 192 | 10 nA | 192
0 | nshort_l | 8/8 | 30,31 | 10 uA | 192 | 1uA | 152 | 100 nA | 192 | 10 nA | 192

## Slide 21: Bank 1 RTS Data Collection Progress
Bank | Type | W/L | Column | Bias Condition | Samples | Bias Condition | Samples | Bias Condition | Samples | Bias Condition | Samples
1 | nshort | 0.28/0.1 | 32,33 | 10 uA | 302 | 1uA | 26 | 100 nA | 34 | 10 nA | 282
1 | nshort | 0.28/8 | 34,35 | 10 uA | 302 | 1uA | 26 | 100 nA | 34 | 10 nA | 202
1 | nshort | 1.5/0.1 | 36,37 | 10 uA | 301 | 1uA | 26 | 100 nA | 34 | 10 nA | 202
1 | nshort | 1.5/0.35 | 38,39 | 10 uA | 300 | 1uA | 26 | 100 nA | 34 | 10 nA | 202
1 | nshort | 1.5/1.6 | 40,41 | 10 uA | 300 | 1uA | 26 | 100 nA | 34 | 10 nA | 202
1 | nshort | 1.5/8 | 42,43 | 10 uA | 300 | 1uA | 26 | 100 nA | 34 | 10 nA | 202
1 | nshort | 8/0.1 | 44,45 | 10 uA | 300 | 1uA | 26 | 100 nA | 34 | 10 nA | 202
1 | nshort | 8/8 | 46,47 | 10 uA | 300 | 1uA | 26 | 100 nA | 34 | 10 nA | 202
1 | nshort_l | 0.28/0.1 | 48,49 | 10 uA | 300 | 1uA | 26 | 100 nA | 34 | 10 nA | 202
1 | nshort_l | 0.28/8 | 50,51 | 10 uA | 300 | 1uA | 26 | 100 nA | 34 | 10 nA | 202
1 | nshort_l | 1.5/0.1 | 52,53 | 10 uA | 300 | 1uA | 26 | 100 nA | 34 | 10 nA | 202
1 | nshort_l | 1.5/0.35 | 54,55 | 10 uA | 300 | 1uA | 26 | 100 nA | 34 | 10 nA | 202
1 | nshort_l | 1.5/1.6 | 56,57 | 10 uA | 300 | 1uA | 26 | 100 nA | 34 | 10 nA | 202
1 | nshort_l | 1.5/8 | 58,59 | 10 uA | 300 | 1uA | 26 | 100 nA | 34 | 10 nA | 202
1 | nshort_l | 8/0.1 | 60,61 | 10 uA | 300 | 1uA | 26 | 100 nA | 34 | 10 nA | 202
1 | nshort_l | 8/8 | 62,63 | 10 uA | 300 | 1uA | 26 | 100 nA | 34 | 10 nA | 202

## Slide 22
Bank | Type | W/L | Column | Bias Condition | Samples | Bias Condition | Samples | Bias Condition | Samples | Bias Condition | Samples
2 | nthickbc | 0.42/0.35 | 64,65 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
2 | nthickbc | 0.42/8 | 66,67 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
2 | nthickbc | 1.2/0.35 | 68,69 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
2 | nthickbc | 1.2/0.5 | 70,71 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
2 | nthickbc | 1.2/0.8 | 72,73 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
2 | nthickbc | 1.2/8 | 74,75 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
2 | nthickbc | 8/0.35 | 76,77 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
2 | nthick | 8/8 | 78,79 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
2 | nthick | 0.42/0.35 | 80,81 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
2 | nthick | 0.42/8 | 82,83 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
2 | nthick | 1.2/0.35 | 84,85 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
2 | nthick | 1.2/0.5 | 86,87 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
2 | nthick | 1.2/0.8 | 88,89 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
2 | nthick | 1.2/8 | 90,91 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
2 | nthick | 8/8 | 92,93 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
2 | nthickbc | 8/8 | 94,95 | 10 uA | 192 | 1uA | 296 | 100 nA | 0 | 10 nA | 0
Bank 2 RTS Data Collection Progress